## Slide 1
ARCHITECTURE STUDIO · DESIGN 4 · STANDARDS STUDY
ARCHITECTURAL STANDARDS OF
SPORTS FACILITIES &
PHYSICAL EDUCATION FACULTY
Space · dimensions · circulation · zoning — every standard shown as
NUMBER + VISUAL + EXPLANATION + SOURCE
PART 01
Sports facilities — basketball & volleyball
PART 02
Physical Education Faculty
PART 03
Comparative standards + references
28.00 m
15.00 m
FIBA court 28 × 15 m + 2 m boundary lane
≥ 7 m
Clear height above court (FIBA) — section
All standards cited on-slide · full references on final slide · 2026

## Slide 2: Ten functional parts organised around one large clear-span volume
01 — SPORTS FACILITY ANATOMY
PUBLIC FRONT
entrance · foyer · reception · WC
SPECTATORS — seating · aisles · accessible spaces
PLAYING SPACE
court + safety / free zone
CHANGING
+ SHOWERS
WARM-UP
OFFICIALS
FIRST AID
EQUIPMENT
STORE
CLEANING
STAFF
SECURITY
CONTROL
SERVICE ENTRANCE · LOADING
PLAYER
ENTRANCE
Diagram — architectural interpretation (not to scale) of the space groups listed in Sport England sports-hall guidance.
Public / spectators
Playing space
Athletes (controlled)
Support / service
THE HALL MODULE
34.5 m
20.0 m
7.5 m
34.5 × 20.0 × 7.5 m
Recommended 4-court hall — Sport England's minimum for school projects; replaces the older 33 × 18 m hall.
RECOMMENDED GUIDELINE
SOURCE Sport England, Sports Halls: Design & Layouts (2012 update) — revised 4-court hall 34.5 × 20.0 × 7.5 m.

## Slide 3: Basketball court 28 × 15 m inside a 2 m obstruction-free boundary lane
02 — BASKETBALL · PLAYING SPACE
28.00 m — court length
15.00 m
2 m
2 m
TEAM A BENCH · 16 seats
TEAM B BENCH · 16 seats
SCORER'S TABLE
Others ≥ 2 m behind team bench → spectator front row starts beyond this line
Plan — diagram redrawn based on FIBA OBR 2024, Diagram 1. Key and arc markings drawn schematically; only dimensioned values are cited.
28 × 15 m
Court, measured from inner edge of boundary line; 'flat, hard surface free from obstructions'.
INTERNATIONAL COMPETITION STANDARD
≥ 2 m
Obstruction-free boundary lane around the court → whole floor ≥ 32 × 19 m.
≥ 7 m
Height of ceiling / lowest obstruction above the court (lights, ducts, trusses).
16 seats
Per team bench area, marked outside the court on the scorer's-table side.
7 m
Section — clear height governs roof structure depth
SOURCE FIBA, Official Basketball Rules 2024 (v1.0) — Rule One, Art. 2 'Court' & Diagram 1; Art. 2.4.5 team bench areas; 'Basketball Equipment' — playing floor.
WHY IT MATTERS The 32 × 19 m floor + 7 m clear height fixes the minimum structural bay and roof depth; storage, benches and seating must all sit outside the 2 m lane.

## Slide 4: Seating section: seat, row, riser, aisle and sightline (C-value)
03 — BASKETBALL · SPECTATOR AREA
COURT
point of focus
(touchline)
2 m lane + bench zone
C = vertical clearance of sightline
over the head in front
row depth ≥ 700 mm
riser = from C-value calc.
radial gangway ≥ 1.2 m (see plan) →
accessible
platform
Section — diagram redrawn based on Green Guide Ch. 12 sightline geometry (rows/risers drawn schematically; riser height is calculated, not fixed).
C = D(N + R) / (D + T) − R
D = horizontal eye-to-focus distance · N = riser · R = eye height above focus · T = row depth
PLAN — SEATING ROW
500
gangway
≥ 1200
WHEELCHAIR SPACE
companion
1400
900
500 mm
Seat width, new construction (460 mm existing).
≥ 700 mm
Seating row depth.
90 mm (60 min.)
C-value for new seated areas: 90–120 mm; 60 mm practical minimum.
≤ 28 seats
Per row between two gangways (≤ 14 with a gangway on one side); gangway ≥ 1.2 m.
1400 × 900 mm
Wheelchair-user spectator space, with companion seat alongside.
RECOMMENDED GUIDELINE (UK)
SOURCE SGSA, Guide to Safety at Sports Grounds ('Green Guide'), 6th ed. 2018, Ch. 12 Seated accommodation; SGSA Supplementary Guidance SG01 (2022). Wheelchair space: Sport England, Accessible Sports Facilities — Design Guidance Note (2010): wheelchair spectator space.
WHY IT MATTERS Sightlines, not seat counts, set the rake: rake + row depth decide hall height, stair geometry and the depth of the spectator zone beside the court.

## Slide 5: Controlled athlete sequence + a service spine that never crosses the public
04 — BASKETBALL · ATHLETES, CHANGING & SUPPORT
ATHLETE SEQUENCE
PLAYER ENTRANCE
CHANGING ROOM
SHOWERS / WC
WARM-UP
SPORTS HALL
OFFICIALS' ROOM
COACHES / TEAM AREA
FIRST AID / MEDICAL
direct, step-free route to court AND to an external ambulance point
Bench: 16 seats / team (FIBA Art. 2.4.5) — team area sits between the athlete corridor and the court.
SUPPORT / BACK-OF-HOUSE ZONING
SPORTS HALL
EQUIPMENT
STORE
(floor level,
wide doors)
CLEANING
SERVICE ENTRANCE
+ LOADING
CHANGING
+ OFFICIALS
FIRST AID
STAFF ROOM
SECURITY / CONTROL
PUBLIC FOYER
Zoning diagram — architectural interpretation; positions are relational, not dimensional.
Store → hall
Equipment store opens directly onto the playing floor at the same level.
Service ≠ public
Loading and cleaning reach the hall without crossing foyer or spectators.
Control point
Security sits at the junction of public foyer and controlled zones.
Medical
First aid is adjacent to both changing and court; ambulance access outside.
SOURCE Planning principles — Sport England, Sports Halls: Design & Layouts (2012) support accommodation; Sport England AISF Part D (2024). Bench: FIBA, Official Basketball Rules 2024 (v1.0) Art. 2.4.5.
No dimensions are shown for support rooms: sizes depend on brief and capacity; none were verified as fixed standards for this study.

## Slide 6: Volleyball 18 × 9 m: free zone + 12.5 m height decide if a hall can host official play
05 — VOLLEYBALL · PLAYING SPACE, HEIGHT & HALL FIT
18 m
9 m
3 m
3 m
6.5
5 m
NET / CENTRE LINE
attack lines 3 m from centre line · all lines 5 cm wide
Court 18 × 9 m
Min. free zone 3 m → 24 × 15 m
FIVB / World / Official: 5 m sides, 6.5 m ends → 31 × 19 m
Plan — diagram redrawn based on FIVB Rules 2025–28, Rule 1 & Diagram 1a/1b.
SECTION — FREE PLAYING SPACE
7 m general
7.5 m SE hall
12.5 m FIVB official
net 2.43 m (men)
2.24 m (women)
HALL FIT-CHECK (SE 34.5 × 20 × 7.5 m)
Layout | Footprint | Fits?
Volleyball + 3 m | 24 × 15 m · 7 m | YES
Volleyball FIVB | 31 × 19 m · 12.5 m | PLAN ✓ HEIGHT ✗
Basketball + 2 m | 32 × 19 m · 7 m | YES
CALCULATION FROM CITED VALUES
A standard 4-court hall accepts every court in plan, but only competition-grade volume (≥ 12.5 m) hosts FIVB-level play → decide the competition level BEFORE fixing roof height.
SPECTATORS · PLAYERS · SUPPORT
Spectators: same Green Guide seat/row/C-value rules as slide 04; front row starts beyond the free zone (5 / 6.5 m at official level).
Players: team benches beside the scorer's table, outside the free zone (Rule 1.4).
Changing / support: identical sequence to basketball — the hall is shared.
SOURCE FIVB, Official Volleyball Rules 2025–2028 — Rule 1 'Playing Area' (1.1 dimensions & free zone, 1.1.2 free playing space, 1.3 lines, 1.4 zones). Hall: Sport England, Sports Halls: Design & Layouts (2012 update) — revised 4-court hall 34.5 × 20.0 × 7.5 m.
TYPES 18 × 9 m, 3 m free zone, 7 m height = rule for all play · 5 / 6.5 m + 12.5 m = FIVB, World & Official competitions only.

## Slide 7: Three separate flows meet only at the court edge — and only by design
06 — CIRCULATION SYSTEMS
SPORTS HALL
SPECTATOR SEATING
RECEPTION · FOYER · WC
CHANGING
SHOWERS · WC
WARM-UP
STORAGE
EQUIPMENT
PLANT
PLAYER
ENTRANCE
MAIN ENTRANCE
EXIT
SERVICE
ENTRANCE
controlled crossing
(court edge only)
Circulation diagram — architectural interpretation (principle, not a specific building).
ATHLETE
Player entrance → changing → shower → warm-up → court
PUBLIC
Main entrance → reception → spectator zone → seating → exit
SERVICE
Service entrance → storage → equipment → sports hall
DESIGN RULES
Separate entrances on different façades.
Spectators never pass through changing or store zones.
Service reaches the hall floor level without steps.
Exits sized and located per fire regulation (INBR Topic 3) — verify for the chosen occupancy.
SOURCE Principle drawn from Sport England sports-hall guidance (zoning of changing, storage, spectator & public areas); fire exits — INBR Topic 3 (Mabhas 3, fire protection).

## Slide 8: Dry → transition → wet: a one-way sequence from entrance to hall
07 — CHANGING ROOMS + SHOWERS + ATHLETE SUPPORT
LOCKERS
500 / person
BENCH + HOOKS
750
COMMUNAL SHOWERS
cubicle
800 min.
900 pref.
DRYING ZONE
(transition, drained floor)
WC
WC
ENTRY
from athlete
corridor
TO WARM-UP /
SPORTS HALL
DRY ZONE
WET ZONE
Plan — illustrative layout by the author; only the labelled component dimensions (mm) are cited. Room size is not a standard.
500 mm
Bench length per person (changing).
750 mm
Spacing between heads, communal shower.
800 / 900
Min. / preferred manoeuvring width in a shower cubicle (mm).
TYPICAL PLANNING VALUE
Values as quoted from Sport England changing guidance by UK changing-room specifiers — verify in the current Sport England note before use.
ACCESSIBLE CHANGING
Provide a separate accessible changing room with its own WC + shower on the same step-free route; Sport England AISF Part D sets layouts and grab-rail positions.
ATHLETE FLOW
CHANGING
SHOWER
WC
WARM-UP
HALL
SOURCE Component values — Sport England changing-room guidance as cited by UK suppliers (e.g. sportschangingrooms.co.uk); accessible provision — Sport England, Accessible & Inclusive Sports Facilities — Part D: Changing & toilet provision (2024).
WHY IT MATTERS Wet and dry zones must not overlap: the drying zone is the threshold that keeps the locker floor dry and defines the one-way route to the hall.

## Slide 9: Four functional groups under one entrance — each with its own critical adjacency
08 — PHYSICAL EDUCATION FACULTY · SPACE RELATIONSHIPS
FACULTY · ENTRANCE + FOYER
EDUCATIONAL
CLASSROOMS
LIBRARY
AUDITORIUM
SOCIAL
CAFETERIA
LOUNGE
INFORMAL STUDY
SPORTS
SPORTS HALL
CHANGING
SHOWERS
EQUIPMENT
SUPPORT
ADMINISTRATION
STORAGE
SERVICES
WC
SERVICE ACCESS
KEY ADJACENCIES
SPORTS HALL ↔ CHANGING direct · HALL ↔ EQUIPMENT direct, same level · CLASSROOMS ↔ LIBRARY near · CAFETERIA ↔ SERVICE direct · AUDITORIUM ↔ FOYER direct (event use)
FIVE USER STREAMS
PUBLIC
foyer → auditorium / events → spectators
STUDENTS
foyer → classrooms, library, cafeteria
ATHLETES
entrance → changing → hall / fields
STAFF
admin ↔ classrooms ↔ labs
SERVICE
yard → kitchen, stores, plant
Adjacency diagram — architectural interpretation; distances not scaled.
SOURCE Space groups as defined in the studio brief; adjacency logic consistent with Sport England sports-hall guidance (hall–changing–store) and university space-planning guides. No numerical standard on this slide.

## Slide 10: Teaching rooms sized per place, side-lit, entered from a 1.8 m corridor
09 — FACULTY · CLASSROOM + LIBRARY
DAYLIGHT (left of writing hand)
BOARD / SCREEN
TEACHER ZONE
1.80 m
CORRIDOR
(educational)
8.0 m
6.9 m
55 m² / 30 places ≈ 1.8 m² per place — example proportions by author; area from BB103.
55 m²
General classroom for 30 (school guideline, used as a lower bound).
2.5–2.75 m²
Per workplace — group-work / IT / seminar rooms (university guide).
1.80 m
Min. corridor width, educational spaces.
RECOMMENDED
MANDATORY (IRAN)
LIBRARY — ZONING PLAN
ENTRY +
SERVICE DESK
BOOK STACKS
QUIET ZONE — individual carrels along daylight façade
READING
TABLES
GROUP STUDY
(enclosed — acoustic)
Noise gradient: loud (entry, group) → quiet (carrels). Accessible route ≥ 1.5 m turning space at desk and stacks.
Area per reader: no authoritative value verified for this study — not presented as a standard.
SOURCE UK DfE, Building Bulletin 103 — Area guidelines for mainstream schools (2014): general classroom 55 m² / 30 pupils. University of York, Space Guidelines & Standards (Aug 2025) — m² per workplace by room type. Corridor: Iranian National Building Regulations (INBR), Topic 4 'General Building Requirements' (Mabhas 4), ed. 1396/2017.

## Slide 11: Rows limited by seatway width; food moves one way from kitchen to waste
10 — FACULTY · AUDITORIUM + CAFETERIA + STUDENT SPACES
AUDITORIUM — SECTION
STAGE
sightline to stage edge → riser grows with distance
WHEELCHAIR
SPACES at rear
Section — schematic; riser from sightline calculation.
PLAN — ROW LENGTH vs SEATWAY
aisle
aisle
seatway ≥ 300
14 seats between two aisles
Seatway (mm) | Aisle one side | Aisles both sides
300 – 324 | 7 seats | 14 seats
425 – 449 | 12 seats | 24 seats
SOURCE BSI, BS 9999 Fire safety in the design, management and use of buildings — seating: seatway width vs. seats per row table.
CAFETERIA — PLAN + SERVICE SEQUENCE
KITCHEN
STORE
RETURN / WASTE
SERVERY
SERVICE ENTRANCE ↓
students in
KITCHEN
SERVICE
DINING
RETURN / WASTE
Plan — illustrative zoning by author. Area per seat: no authoritative value verified → derive from table + chair + aisle layout (Neufert, 'Restaurants').
STUDENT / SOCIAL
LOUNGE
between teaching and sport — the faculty's social hinge
INFORMAL STUDY
edges of corridors & atria, daylit, visible
COMMON SPACE
shared foyer for auditorium + cafeteria events
AUDITORIUM CHECKLIST
Wheelchair spaces 1400 × 900 mm (SE 2010)
Exits at stage end + rear, sized per INBR Topic 3
Acoustic separation from sports hall
WHY IT MATTERS Row length is a fire-escape rule, not a comfort choice; the cafeteria needs its own service yard so food and waste never cross the student route.

## Slide 12: Iranian minimums shown beside the UK reference — both dimensioned
11 — SANITARY SPACES + ACCESSIBILITY
ACCESSIBLE WC — IRAN (min.)
WC
grab rail
170 cm
150 cm
door 90 cm
Ø150 turning
circle
MANDATORY (IRAN) · VERIFY EDITION
SOURCE Supreme Council of Urban Planning & Architecture of Iran — 'Urban & architectural regulations for people with physical-motor disabilities'.
ACCESSIBLE WC — UK REFERENCE
WC
basin
1500 mm
2200 mm
1500 turning
circle
MANDATORY (UK)
SOURCE HM Government, Approved Document M, Vol. 2 (2015 ed.) — Diagram 18, wheelchair-accessible unisex WC.
STANDARD WC · BASIN · SHOWER
BASINS — circulation zone in front kept clear of door swings
Not dimensioned: cubicle and basin sizes were not verified from an authoritative source for this study (see Neufert 'Sanitary facilities').
STAIR · RAMP · CORRIDOR (IRAN)
10–18 cm
≥ 28 cm
2R + T = 63–64 cm · headroom ≥ 205 cm
ramp ≤ 8 % · run ≤ 3 m · rise ≤ 25 cm · width ≥ 120 cm
Corridor: ≥ 1.80 m educational · ≥ 1.40 m main accessible route
SOURCE Stairs & corridors — Iranian National Building Regulations (INBR), Topic 4 'General Building Requirements' (Mabhas 4), ed. 1396/2017. Ramp — Iranian accessibility regulations (above). Values cross-checked only via published summaries → confirm in official text.

## Slide 13: Where Iranian and international values differ — and why
12 — COMPARATIVE STANDARDS
Requirement | Iranian source | International source | Type | Why they may differ
Accessible WC (min. room) | 170 × 150 cm Iran accessibility regs | 150 × 220 cm UK ADM Vol. 2, Diag. 18 | Mandatory (both) | UK room contains basin + side transfer space + full 1500 turning circle; Iranian minimum is a compact WC-only room.
Stair clear width | ≥ 110 cm (INBR Topic 4 summary) ≥ 115 cm (other summary) | — (not compared) | Mandatory | Two secondary summaries disagree → official 1396 text must be checked; width also depends on occupant load (Topic 3).
Corridor, educational | ≥ 180 cm INBR Topic 4 | — (BB103 sets areas, not widths) | Mandatory | Iran fixes a width for school/university corridors; UK guidance works through area budgets and fire design.
Basketball clear height | Not verified (Ministry of Sport & Youth guidelines not accessible) | ≥ 7 m FIBA · 7.5 m Sport England hall | Competition / recommended | FIBA = playing rule; Sport England adds margin for badminton & multi-use.
Volleyball clear height | Not verified | 7 m (all) · 12.5 m FIVB official | Competition | Level of play: World/Official events need high-ball space.
Spectator seat width | Not verified | 460 mm existing · 500 mm new (Green Guide) | Recommended | UK guidance raised comfort/safety for new build.
Classroom area | Not verified for universities | 55 m² / 30 (BB103) · 2.5–2.75 m²/place (Univ. York) | Recommended | School vs university norms; furniture & pedagogy differ.
MANDATORY REGULATION
RECOMMENDED GUIDELINE
INTERNATIONAL COMPETITION STANDARD
TYPICAL PLANNING VALUE
CALCULATION
Red text = value could not be verified or sources conflict — not presented as a standard.
SOURCE See full references (next slide). Iranian values were checked through published summaries of INBR Topic 4 and the Supreme Council accessibility regulations; the printed official editions remain the authority.

## Slide 14: Sources cited on the slides
13 — REFERENCES
IRANIAN SOURCES
Iranian National Building Regulations, Topic 3 — Fire protection Ministry of Roads & Urban Development, latest ed.
مبحث ۳ — حفاظت ساختمان‌ها در مقابل حریق
Iranian National Building Regulations, Topic 4 — General building requirements, 1396 / 2017 ed.
مبحث ۴ — الزامات عمومی ساختمان
Iranian National Building Regulations, Topics 15 (elevators), 19 (energy), 22 (maintenance) — consulted for scope; no values cited.
Supreme Council of Urban Planning & Architecture of Iran — Urban & architectural regulations for people with physical-motor disabilities.
ضوابط و مقررات شهرسازی و معماری برای افراد دارای معلولیت جسمی-حرکتی
Ministry of Sport & Youth — sports facility guidelines: NOT ACCESSIBLE for verification in this study; flagged on slide 12.
INTERNATIONAL SOURCES
FIBA, Official Basketball Rules 2024 & Basketball Equipment.
https://assets.fiba.basketball/image/upload/documents-corporate-fiba-official-rules-2024-v10a.pdf
FIVB, Official Volleyball Rules 2025–2028.
https://www.fivb.com/wp-content/uploads/2025/01/FIVB-Volleyball_Rules2025_2028-EN-v05.pdf
Sport England, Sports Halls: Design & Layouts (2012).
https://sportengland-production-files.s3.eu-west-2.amazonaws.com/s3fs-public/sports-halls-design-and-layouts-2012.pdf
Sport England, Accessible Sports Facilities (2010).
https://sportengland-production-files.s3.eu-west-2.amazonaws.com/s3fs-public/accessible-sports-facilities-2010.pdf
Sport England, AISF Part D — Changing & toilet provision (2024).
https://sportengland-production-files.s3.eu-west-2.amazonaws.com/s3fs-public/2024-08/AISF-Part-D-Changing-and-toilet-provision.pdf
SGSA, Guide to Safety at Sports Grounds, 6th ed. (2018) & SG01 (2022).
https://sgsa.org.uk/document/greenguide/
BSI, BS 9999 — Fire safety in the design, management & use of buildings (seating).
https://knowledge.bsigroup.com
HM Government, Approved Document M Vol. 2 (2015 ed.).
https://www.gov.uk/government/publications/access-to-and-use-of-buildings-approved-document-m
DfE, Building Bulletin 103 — Area guidelines for mainstream schools (2014).
https://dera.ioe.ac.uk/id/eprint/20283/1/BB103_Area_Guidelines_for_Mainstream_Schools_FINAL_23_4_14.pdf
University of York, Space Guidelines & Standards (Aug 2025).
https://www.york.ac.uk/media/campusdevelopment/63697_UniofYork%20Space%20Guidelines%20and%20Standards%20v2.pdf
Neufert, Architects' Data (Wiley) · Metric Handbook (Routledge) · Architectural Graphic Standards (Wiley) — general planning references; no values cited where not verified.
World Aquatics rules not used — no pool standards are presented in this study.