## Slide 1
ARCHITECTURE STUDIO · DESIGN 4 · PRECEDENT ANALYSIS
HOW ARE SPORT,
LEARNING AND
SERVICE ORGANISED?
Spatial analysis of two precedents for a Faculty of Physical Education
CASE 01 — PRIMARY
Anna Pao Sohmen Centre, YK Pao School, Shanghai
Scenic Architecture Office
CASE 02
Faculty of Physical Education and Sport, Charles University, Prague
Photo: Anna Pao Sohmen Centre — uploaded set (p. 28)
Key question: why are these spaces organised this way, and what can a faculty design learn from it?

## Slide 2: Plans first: every reading is tagged VERIFIED or INTERPRETATION
00 — CASE STUDIES + METHOD
01
COLLECT
Uploaded drawings & photos (Case 01) are the primary source; publications fill gaps.
02
READ PLANS
Identify levels, rooms (translated from drawing legends), entrances, cores.
03
OVERLAY
Colour-coded zoning + circulation drawn over the original plans.
04
RELATE
Adjacency, public → private gradient, section stacking.
05
EXTRACT
Design principles → lessons for a PE Faculty.
CASE 01 · PRIMARY
Anna Pao Sohmen Centre
Shanghai, China · Scenic Architecture Office · 2025
Full drawing set available: 6 plans, 3 sections, 2 axonometrics, site plan.
Documentation gap —
no plans published
CASE 02
FTVS, Charles University
Prague 6 – Veleslavín, Czech Republic
No published floor plans or sections could be obtained → analysis limited to campus & programme level.
ZONE COLOURS (used on every slide)
Public
Semi-public / education
Controlled / private
Sports
Service
CIRCULATION
Public / students
Sports users
Service
VERIFIED
from drawings or a cited publication
ARCHITECTURAL INTERPRETATION
reading of the plan

## Slide 3: A six-level 'vertical campus' of sport, making and gathering on a tight school site
CASE 01 — ANNA PAO SOHMEN CENTRE · PROJECT
Entrance façade (p. 1) · lifted volume over the field (p. 28)
Project | Anna Pao Sohmen Centre at YK Pao School | AD
Architect | Scenic Architecture Office (SAO) | AD
Location | Shanghai, China — school campus on Hongqiao Road (虹桥路, site plan) | AD + drawing
Completed | 2025 | AD
Area | 2,473 m² (ArchDaily) · GFA 7,911.8 m² = 6,945.5 above + 966.3 basement (gooood) | SOURCES DIFFER
Levels | B1 · GF · 2F mezzanine · 3F · 4F · roof court = 6 levels | drawings
Programme | Indoor pool, multi-purpose basketball hall, table tennis, roof sports court; STEAM classrooms (art, music, ICT, wood, robotics, fashion, photography); teacher-training centre; collective hub / lecture space | AD / gooood
Institution | YK Pao School — school campus (age groups not verified) | AD
CONCEPT (as published)
“The upper mass floats above the synthetic turf field, with angled concrete columns carrying the load while keeping the ground level open” — building upward to add six levels of programme while increasing usable outdoor area.
Area: the two published figures cannot both be gross floor area; 2,473 m² likely refers to a footprint/site figure — NOT VERIFIED. Use GFA only with its source.
SOURCE ArchDaily, 'Anna Pao Sohmen Centre at YK Pao School / Scenic Architecture Office' (2025) — archdaily.com/1041795 · gooood, 'Anna Pao Sohmen Centre at Shanghai YK Pao School by Scenic Architecture Office' — gooood.cn · Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48)

## Slide 4: Placed at the hinge between campus lawn and sports field, close to the main gate
CASE 01 — SITE + CONTEXT
ANNA PAO SOHMEN CENTRE
HONGQIAO ROAD (虹桥路)
school main entrance
secondary entrance
building entrance
SPORTS FIELD + TRACK
CENTRAL LAWN
low-rise residential
Site plan (uploaded p. 46) — annotations translated from the Chinese labels: 学校主入口 main school entrance · 学校次入口 secondary entrance · 主入口 building entrance.
VERIFIED
Road (Hongqiao Rd.), school main & secondary entrances and the building's main entrance are labelled on the site plan. North arrow and 0–30 m scale on drawing. Building sits between the school buildings, the lawn and the field with 400 m-type track (drawn).
ARCHITECTURAL INTERPRETATION
The centre is the 'turn' of the campus: entered from the lawn side, it opens on the other side to the field — a hinge, not an object.
Short walk from the main gate → doubles as a public/event building without crossing the teaching campus.
Tight footprint between existing buildings and the field explains the vertical stacking and the lift-up over the track.
Vehicular / service access: NOT VERIFIED from the site plan.
Orientation / solar strategy: NOT VERIFIED from published sources.
SOURCE Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48) — site plan; ArchDaily, 'Anna Pao Sohmen Centre at YK Pao School / Scenic Architecture Office' (2025) — archdaily.com/1041795

## Slide 5: Build up, free the ground: the field continues under the building
CASE 01 — ARCHITECTURAL CONCEPT
Exploded axonometric — architects' drawing (p. 39)
Covered field under the 3F–4F volume; angled concrete columns at the track edge (pp. 26, 5)
CONCEPT DIAGRAM
A · object beside the field
B · stacked + lifted: field runs under, roof becomes a court
ARCHITECTURAL INTERPRETATION
Upper floors (3F–4F) cantilever south over the track — dashed outline on the GF plan matches the 3F footprint.
Sports volumes stacked: pool (GF/B1) → gym (3F–4F) → roof court.
Learning wraps the gym on three sides → daylight + views (ArchDaily).
SOURCE ArchDaily, 'Anna Pao Sohmen Centre at YK Pao School / Scenic Architecture Office' (2025) — archdaily.com/1041795 (quoted concept); Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48); Photographs: uploaded set (pp. 1–32), as published with the project

## Slide 6: GF: an assembly lobby between pool and field; wet + service behind
CASE 01 — GROUND FLOOR PLAN
E
F
E entrance (from site plan) · F opens to field under the cantilever · ▭ cores
ROOMS (drawing legend, translated)
1 Assembly lobby · 2 Storage · 3 Toilet · 4 Pool foyer · 5 Change rooms · 6 Swimming pool · 7 Equipment · 8 Emergency clinic · 9 Office · 10 Staff lounge · 11 Power distribution
Public
Semi-public / education
Controlled / private
Sports
Service
Public / students
Sports users
Service
VERIFIED
Pool hall is the largest GF space; change rooms sit between pool and pool foyer; clinic, office, storage and equipment line the north edge; a staircase rises from the lobby to the 2F mezzanine.
ARCHITECTURAL INTERPRETATION
WHY the lobby here: it is the threshold between campus (entrance) and field (south) — gathering space that also distributes to the pool and upper floors.
Direct access: pool foyer → change rooms → pool (wet sequence never re-enters the dry lobby).
Controlled: clinic & staff rooms at the back edge, near the north stair.
Service: plant + storage stacked on the north strip, power room detached — away from public frontage.
Acoustic / humidity: pool enclosed by service & change rooms rather than by classrooms.
SOURCE Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48) — Ground Floor Plan (p. 40). Zones, arrows and pins added by author.

## Slide 7: Below: plant under the pool. Above: a mezzanine that watches the pool and the field
CASE 01 — BASEMENT + SECOND FLOOR
BASEMENT — equipment rooms (设备间) all round the void under the pool (泳池下方管道空腔)
Note: drawing's English legend reads 'Activity mezzanine' for item 1; the Chinese 设备间 = equipment room → used here.
2F — 1 Activity mezzanine · 2 Table tennis · 3 Storage · 4 Equipment; dashed = pool void below
Table tennis looks into the pool through the wave windows (p. 10) · lobby stair-seating to mezzanine (p. 25)
VERIFIED
B1 contains only equipment rooms and the pipe void beneath the pool. 2F: mezzanine over the lobby, table-tennis room above the change rooms, equipment strip along the north; an external bridge/stair leaves the east side.
ARCHITECTURAL INTERPRETATION
Service stacked under service: B1 plant directly below the pool → shortest pipe runs, no plant on public levels.
Visual connection: table tennis overlooks the pool; mezzanine overlooks lobby + field → sport is displayed, not hidden.
The lobby stair is also seating (photo) → circulation doubles as spectator space.
SOURCE Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48) — Basement (p. 42) & Second Floor (p. 35) plans; Photographs: uploaded set (pp. 1–32), as published with the project

## Slide 8: 3F: the gym as the centre, wrapped by classrooms, offices and an atrium ring
CASE 01 — THIRD FLOOR PLAN
C
A
A atrium void with roof light · C pomelo courtyard (open) · ▭ cores
ROOMS (drawing legend)
1 Atrium · 2 Storage · 3 Toilet · 4 Indoor gym · 5 Change room · 6 Classroom · 7 Equipment · 8 Multi-function room · 9 Seminar · 10 Office · 11 Pomelo courtyard
Public
Semi-public / education
Controlled / private
Sports
Service
Public / students
Sports users
Service
Atrium + oval roof light (p. 21)
VERIFIED
Gym (4) occupies the centre-north; classrooms + courtyard on the west; multi-function, seminar and offices on the south façade; change rooms + toilets between gym and offices; a sculptural stair + lift form the SW core.
ARCHITECTURAL INTERPRETATION
Gym = organising mass; every other room is a 'liner' along a façade → daylight for learning, gym lit from roof/high windows.
Change rooms (5) sit on the atrium side of the gym → sports users enter the gym without crossing classrooms.
Atrium ring = public spine: links core, multi-function hall (event use), seminars and gym doors.
Courtyard splits the classroom wing → light, air and a quiet outdoor pause.
Offices at the SE corner: controlled, next to the external stair rather than the public core.
SOURCE Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48) — Third Floor Plan (p. 33). Overlay by author.

## Slide 9: 4F studios ring the gym void; the roof is a second, open-air court
CASE 01 — FOURTH FLOOR + ROOF
4F — studios: visual art, ICT, robotics, maker, wood, greenhouse, fashion, photography, dark room, 3D print, recording; dashed = gym void
ROOF — 1 roof playground (court + stepped seats N & S) · 2 activity space · 3 solar equipment platform · 4 clerestory desks
Roof court above the studio façade (p. 3) · pitched-roof wood studio (p. 16)
VERIFIED
4F studios line west and south façades; offices/dark room/photo studio line the gym's west wall. Roof: full court with stepped seating on both long sides, solar plant platform, and 'clerestory desks' over the atrium.
ARCHITECTURAL INTERPRETATION
Noise/mess-tolerant making studios grouped on one floor, above quieter classrooms.
Roof court reuses the gym's footprint → the long-span structure carries play twice.
Stepped seats make the roof a small outdoor arena; clerestory desks = skylights that are also furniture.
Plant (solar) kept to a strip beside the court, away from the play edge.
SOURCE Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48) — Fourth Floor (p. 41) & Roof plans (p. 37); Photographs: uploaded set (pp. 1–32), as published with the project

## Slide 10: Zoning is vertical: wet sport low, dry sport high, learning around, service below
CASE 01 — FUNCTIONAL ZONING
Programme axonometric — architects' drawing and colours (p. 38)
PUBLIC
SEMI-PUBLIC / EDU
CONTROLLED
SPORTS
SERVICE
ROOF
roof court + seats
solar platform
4F
atrium
studios, ICT, art
offices, dark room
(gym void)
equipment, WC
3F
atrium, multi-function
classrooms, seminar
offices, change
indoor gym
storage, WC
2F
mezzanine
table tennis
equipment
GF
assembly lobby
pool foyer
clinic, staff
pool
storage, power
B1
plant under pool
VERIFIED ROOMS · ZONE ASSIGNMENT = INTERPRETATION
SOURCE Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48) — all plans + programme axonometric (p. 38).

## Slide 11: Two hearts — the lobby (GF) and the atrium (3F) — connected by one core
CASE 01 — SPATIAL RELATIONSHIPS / ADJACENCY
CAMPUS LAWN / ENTRANCE
ASSEMBLY LOBBY
FIELD + TRACK
(under building)
POOL FOYER
CHANGE ROOMS
POOL
PLANT (B1)
MEZZANINE (2F)
TABLE TENNIS (2F)
WEST CORE: LIFT + STAIR
ATRIUM (3F–4F)
INDOOR GYM
CHANGE (3F)
CLASSROOMS / STUDIOS
COURTYARD
MULTI-FUNCTION / SEMINAR
OFFICES
ROOF COURT
LINE TYPES
direct / required (plan-verified)
sports sequence
near / shared corridor
visual connection
service (vertical)
ARCHITECTURAL INTERPRETATION
Pool ↔ change ↔ foyer: linear wet sequence on GF (plan).
Gym ↔ change (3F): change rooms open off the atrium beside gym doors.
Lobby ↔ field: lobby glazed + stepped to the track (section p. 34).
Atrium ↔ multi-function / seminar: event rooms on the public ring.
Plant directly below pool: vertical service adjacency.
Table tennis ↔ pool: visual only (wave windows, photo p. 10).
SOURCE Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48) (plans pp. 33–42, section p. 34); Photographs: uploaded set (pp. 1–32), as published with the project

## Slide 12: One public core, one back stair, one external stair — and stairs that are also seats
CASE 01 — CIRCULATION
B1
GF
2F
3F
4F
ROOF
WEST CORE
lift + sculptural stair
NORTH STAIR
(back of house)
EAST EXTERNAL STAIR
lobby stair-seating
3F atrium ring (public spine)
GF lobby
Schematic vertical-circulation diagram, based on cores identified in all plans (not to scale).
Stair with timber screen (p. 23) · atrium stair landing (p. 20)
VERIFIED
Cores in plans: lift + curved stair (SW, all levels GF–4F), north stair (B1–roof), straight stair lobby→2F, east external stair/bridge (2F–3F).
ARCHITECTURAL INTERPRETATION
Students / visitors: lobby → west core or stair-seating → atrium ring → rooms.
Sports users: field/lobby → change rooms → pool or gym without passing studios.
Staff: offices next to the east external stair; north stair as back route.
Service: north stair + equipment strip connect B1 plant to every level.
User-separation by schedule is likely, not by fully separate routes — NOT VERIFIED.
SOURCE Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48); Photographs: uploaded set (pp. 1–32), as published with the project

## Slide 13: Control increases with height and with distance from the lobby
CASE 01 — PUBLIC → PRIVATE GRADIENT
PUBLIC
Field under the building · lobby · stair-seating · mezzanine
open edge to field; lobby doubles as assembly
SEMI-PUBLIC
Atrium ring · multi-function hall · seminars · pool foyer
reached via the public core; event-capable rooms
CONTROLLED
Classrooms · studios · change rooms · clinic
doors off the ring; change rooms gate the sports volumes
PRIVATE / SERVICE
Offices · staff lounge · equipment · plant (B1) · solar platform
edges, back stair, basement and roof strip
↓ increasing control
Courtyard threshold (p. 29) · entrance (p. 31)
ARCHITECTURAL INTERPRETATION
Control is architectural, not only by doors: height (GF open → 4F studios), depth (front lobby → back offices) and sequence (change rooms before courts).
The lobby can open for events while upper teaching floors stay closed — the core is the single checkpoint.
Pool access is gated twice: pool foyer → change rooms.
Service zones never face the lobby: north strip, basement, roof edge.
SOURCE Derived from Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48); Photographs: uploaded set (pp. 1–32), as published with the project

## Slide 14: Three long spans stacked: pool → gym → roof court
CASE 01 — SECTIONAL ORGANISATION
ROOF COURT + seats
INDOOR GYM
POOL
LOBBY
STUDIOS
PLANT
N–S section (p. 36) — overlay by author
E–W section through pool, table tennis, change rooms & courtyard (p. 48) — overlay by author
VERIFIED
Sections show the pool at grade/below grade with plant beneath, the indoor gym as a double-height volume on 3F–4F directly above, and the roof court with stepped seating on top. The assembly lobby + mezzanine sit beside the pool and open to the track.
ARCHITECTURAL INTERPRETATION
Double-height gym sits on a deep transfer floor over the pool → the most demanding spans are stacked, so loads travel straight down.
Wave-shaped pool clerestory: daylight under the gym floor (ArchDaily: arched clerestory windows).
Learning floors (≈ 2 storeys) wrap the gym height → classrooms share the gym's section, not its noise.
The 3F courtyard (with tree) is cut into the stack — outdoor space at upper level.
Floor-to-floor heights NOT dimensioned here: not stated in sources; scaling the drawings would be approximate.
SOURCE Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48) — sections pp. 34, 36, 48; ArchDaily, 'Anna Pao Sohmen Centre at YK Pao School / Scenic Architecture Office' (2025) — archdaily.com/1041795

## Slide 15: Outdoor space at three levels: under, inside and on top of the building
CASE 01 — INDOOR / OUTDOOR + ENVIRONMENT
UNDER — covered field
sport + recreation + shelter
INSIDE — pomelo courtyard (3F)
social + landscape + light
ON TOP — roof court
sport + spectators
EDGE — pool clerestory
daylight + visual link to street
Photos: uploaded set pp. 26, 29, 3, 2
Strategy | Evidence | Status
Daylight to learning spaces | Classrooms 'profit from natural daylighting and scenic views' (ArchDaily); rooms line façades on plans | VERIFIED
Pool daylight | Arched clerestory windows along the pool; timber beams diffuse light (ArchDaily); wave windows in photos/section | VERIFIED
Atrium roof light | Oval atrium + 'clerestory desks' on roof plan; photos p. 20–21 | VERIFIED (drawings)
Green façade / shading | Planted screens and timber-colour grid on façades (photos p. 1–6) | VISIBLE — performance not verified
Solar energy | 'Solar equipment platform' on roof plan | VERIFIED (drawing) — capacity unknown
Natural ventilation / orientation | No published statement | NOT VERIFIED
SOURCE ArchDaily, 'Anna Pao Sohmen Centre at YK Pao School / Scenic Architecture Office' (2025) — archdaily.com/1041795; Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48); Photographs: uploaded set (pp. 1–32), as published with the project

## Slide 16: Long spans stacked on one footprint; angled columns release the ground
CASE 01 — STRUCTURAL / ARCHITECTURAL LOGIC
Angled columns at the field edge (p. 5) · gym roof structure with skylights (p. 12)
POOL span
lobby / mezzanine
GYM span (3F–4F)
ROOF COURT
V / angled
columns
Schematic section — interpretation, not to scale
VERIFIED
Angled concrete columns carry the upper mass over the turf (ArchDaily). Plans show a regular column grid around the gym and pool; sections show a deep structural zone under the gym floor and under the roof court.
ARCHITECTURAL INTERPRETATION
The gym is column-free; its roof is also a playground → a deep, stiff roof structure (visible joists/beams in section).
Pool directly below the gym → the transfer floor between them is the key structural element.
Perimeter rooms are on a smaller grid → structure follows the 'big room + liner' plan.
Material, span and member sizes: NOT VERIFIED (no structural data published).
SOURCE ArchDaily, 'Anna Pao Sohmen Centre at YK Pao School / Scenic Architecture Office' (2025) — archdaily.com/1041795; Drawings: Scenic Architecture Office, as published (uploaded set, pp. 33–48); Photographs: uploaded set (pp. 1–32), as published with the project

## Slide 17: Seven principles extracted from the Anna Pao Sohmen Centre
CASE 01 — KEY DESIGN PRINCIPLES
01
Stack the long spans
Pool → gym → roof court on one footprint frees the site.
02
Lift to give back ground
Upper floors cantilever; the field continues under the building.
03
Big room + liner
Gym in the centre; classrooms / studios line the façades for daylight.
04
Thresholds that gather
Lobby and atrium are distribution AND event spaces (stair-seating).
05
Wet sequence is linear
Foyer → change → pool; dry users never cross wet floors.
06
Show the sport
Visual links: table tennis → pool, mezzanine → field, roof seats → court.
07
Service stacked out of sight
Plant under the pool, equipment strip at the back, solar on the roof edge.
Programme axo (p. 38)
PRINCIPLES = INTERPRETATION OF VERIFIED PLANS

## Slide 18: A faculty inside a converted 1950s complex, with sport spread across a campus
CASE 02 — FTVS, CHARLES UNIVERSITY · PROJECT + CONTEXT
Institution | Faculty of Physical Education and Sport (FTVS / 'CU SPORT'), Charles University | FTVS / CUNI
Address | José Martího 269/31, Praha 6 – Veleslavín, Czech Republic | FTVS contacts
Original building | Built 1949–1956 for the Communist Party's political college (VŠP ÚV KSČ, 'Vokovická Sorbonna') | slavnevily.cz · cs.wikipedia
Use as faculty | Faculty moved here after 1989 (VŠP dissolved 1990); faculty part of Charles University since 1959 | cs.wikipedia
Architecture | 'Strict, originally symmetrical' composition on a functionalist basis | slavnevily.cz
Blocks | Lettered blocks A–H (A–D insulation, E–H façade renewal in a university tender) | zakazky.cuni.cz
Architect | NOT VERIFIED | 
Area / plans | NOT VERIFIED — no published floor plans, sections or areas found | 
CONTEXT — RELATIONAL DIAGRAM
PRAGUE CENTRE
NOVÝ VELESLAVÍN
metro + city district
FTVS COMPLEX
blocks A–H
STADIUM + PITCHES
tennis · beach volley
SPORTS HALL
+ gym rooms
≈ 25 min by
public transport
ARCHITECTURAL INTERPRETATION — relational, not a map
Positions are not geographic. Exact site layout, access points and orientation could not be verified from available documentation.
SITE / CONTEXT READING
A suburban campus in Prague 6, served by the Nový Veleslavín transport hub — the faculty is a destination, not part of the historic university core (verified: location; interpretation: role).
Teaching occupies a building designed for a different institution → sport facilities were added around it rather than integrated in one volume (interpretation).
SOURCE ftvs.cuni.cz (contacts; 'Jak se vyznat na fakultě'); cs.wikipedia.org — VŠP ÚV KSČ & FTVS UK; slavnevily.cz — 'Škola ve Veleslavíně'; zakazky.cuni.cz — FTVS tender; cuni.cz.

## Slide 19: Verified facilities, organised as a campus of separate sports elements
CASE 02 — FUNCTIONAL PROGRAMME, ZONING + STANDARDS CHECK
VERIFIED FACILITIES
Sports hall 22 × 32 m (704 m²), Taraflex floor, multi-court markings
iscus.cz #19361
Gym + gymnastics room
iscus.cz #19361
Stadium: football 100 × 65 m + 400 m track, 6 lanes, jump sectors
iscus.cz #19360
Tennis courts · beach-volleyball court
ftvs.cuni.cz
CU SPORT Gym — basement of block H: reception, weights, stretching, TRX, shooting range + cardio, athletic tunnel, warm-up
ftvs.cuni.cz
'Creative Hub' study room above the gym (block H)
ftvs.cuni.cz
Teaching, departments, administration in blocks A–H
ftvs.cuni.cz
BLOCK H — VERIFIED STACKING
CREATIVE HUB (study)
CU SPORT GYM (basement)
Study above training — a small-scale version of APSC's 'learning over sport'.
SPORTS HALL 32 × 22 m — STANDARDS FIT (to scale)
32 m
22 m
— basketball 28 × 15 + 2 m lane = 32 × 19 m → fits exactly in length
- - volleyball 18 × 9 + 3 m = 24 × 15 m → fits; FIVB official (31 × 19 m) fits in plan
CALCULATION FROM CITED VALUES
Hall clear height: NOT VERIFIED → official FIVB use (12.5 m) cannot be confirmed.
ADJACENCY (programme)
ENTRANCE / ADMIN
TEACHING BLOCKS
CHANGING ?
HALL · GYM
STADIUM · COURTS
INTERPRETATION
Dashed = relationship not verifiable without plans (location of changing rooms, routes between blocks and outdoor facilities).
SOURCE iscus.cz — Haly sportovního centra UK Veleslavín (#19361) & Stadion a venkovní hřiště (#19360); ftvs.cuni.cz — sports facilities, 'CU SPORT Gym'. Court values: FIBA OBR 2024 Art. 2; FIVB Rules 2025–28 Rule 1.

## Slide 20: What can be learned — and what must be obtained before analysing further
CASE 02 — CIRCULATION, SECTION + PRINCIPLES
NOT VERIFIED FROM AVAILABLE DOCUMENTATION
Floor plans
room layout, entrances, cores, changing-room position
Sections
hall clear height, vertical stacking, basement gym depth
Circulation
routes between blocks, sports hall and stadium; athlete vs. public separation
Structure
grid, hall roof span and system
Environment
orientation, daylight, ventilation strategy
HOW TO CLOSE THE GAP
Request plans from the faculty's building-management office (FTVS UK).
Prague 6 building archive — building-permit drawings of José Martího 31.
Site visit: photograph entrances, changing rooms, hall section; pace distances.
PRINCIPLES THAT CAN BE EXTRACTED (programme level)
01
Campus of parts
Teaching blocks + separate hall + outdoor stadium: each sport element sized to its own standard (hall exactly fits a FIBA court + lane).
02
Outdoor sport as a field, not a roof
100 × 65 m pitch with 400 m track needs land — opposite of APSC's vertical strategy.
03
Adaptive reuse
A 1950s symmetrical college re-programmed for sport education; renovation by blocks (A–H).
04
Training under study
Basement gym beneath a study hub in block H — vertical mix at small scale.
INTERPRETATION OF VERIFIED FACTS
SOURCE As previous two slides.

## Slide 21: Vertical compression vs. horizontal campus — two answers to the same programme
COMPARATIVE ANALYSIS
Category | Anna Pao Sohmen Centre (Shanghai) | FTVS Charles University (Prague)
Site organisation | Compact infill between lawn and field; ground freed by lifting | Suburban campus; buildings + separate outdoor sports land
Main entrance | From the lawn into an assembly lobby (site plan) | Not verified
Functional zoning | Vertical: wet sport low, dry sport high, learning wraps | Horizontal (interp.): teaching blocks, hall, stadium as separate parts
Public / private | Height + depth + sequence; lobby = only public threshold | Not verifiable without plans
Circulation | One public core + atrium ring; stairs as seating | Between blocks and outdoors — not verified
Sports spaces | Pool, gym, table tennis, roof court — stacked | Hall 32 × 22 m, gym rooms, stadium 100 × 65 m + track, courts
Educational spaces | STEAM classrooms & studios lining façades | Teaching in converted 1950s blocks A–H
Social spaces | Lobby, mezzanine, atrium, courtyard, roof seats | Creative Hub study room (block H)
Service spaces | Basement plant, north equipment strip, roof solar | Not verified
Indoor / outdoor | Under, inside and on top (field, courtyard, roof) | Outdoor sport on grade beside buildings
Structural logic | Stacked long spans + angled columns | Not verified
Main strategy | Compress & stack → maximise outdoor ground | Distribute & reuse → land-based campus
Not a ranking: APSC shows how to fit a sports-learning programme on scarce land; FTVS shows the land and buildings a full PE faculty with outdoor athletics actually needs.

## Slide 22: Twelve transferable principles — not copies of either building
DESIGN LESSONS FOR A FACULTY OF PHYSICAL EDUCATION
01
FUNCTIONAL ZONING
Zone in section as well as plan: wet sport + plant low, dry halls above, learning on the daylit perimeter.
from: APSC
02
EDUCATION ↔ SPORT
Wrap halls with teaching rooms that look in (glazed screens) but are acoustically separated.
from: APSC
03
STUDENT SOCIAL SPACE
Make the lobby/atrium the social core: stair-seating, mezzanines, courtyard.
from: APSC
04
CIRCULATION
One legible public spine + separate back-of-house stair/lift for service and staff.
from: APSC
05
SPECTATOR / USER SEPARATION
Spectators via lobby & seating; athletes via change rooms that open directly onto courts.
from: APSC + standards
06
CHANGING ROOMS
Place them between entrance and every court/pool: foyer → change → sport, wet never crossing dry.
from: APSC
07
HALL ADJACENCY
Hall ↔ change ↔ store at the same level; size hall to FIBA 32 × 19 m min. footprint.
from: FTVS + FIBA
08
SERVICE ACCESS
Plant and storage stacked behind or below; a service yard away from the public front.
from: APSC
09
OUTDOOR SPORT
Reserve land for a 400 m track & pitch if athletics is taught; otherwise use roofs/undercrofts.
from: FTVS vs APSC
10
PUBLIC / PRIVATE
Grade control by height and depth; let the ground floor open for events.
from: APSC
11
COURTYARDS + LANDSCAPE
Cut courtyards into upper floors to light deep plans and give quiet outdoor rooms.
from: APSC
12
FLEXIBLE + LARGE-SPAN
Stack long spans on one footprint; multi-court halls; reuse existing buildings where possible.
from: APSC + FTVS
All lessons are architectural interpretations derived from the analysed plans, sections and verified facts; dimensional rules come from the standards study (FIBA / FIVB / Sport England / INBR).

## Slide 23: Sources used in the case-study analysis
REFERENCES
CASE 01 — ANNA PAO SOHMEN CENTRE
Uploaded drawing & photo set (CamScanner PDF, 64 pp.): plans GF, 2F, 3F, 4F, roof, basement; sections; axonometrics; site plan — Scenic Architecture Office.
ArchDaily — Anna Pao Sohmen Centre at YK Pao School / Scenic Architecture Office (2025).
https://www.archdaily.com/1041795/anna-pao-sohmen-centre-at-yk-pao-school-scenic-architecture-office
gooood — Anna Pao Sohmen Centre at Shanghai YK Pao School by Scenic Architecture Office.
https://www.gooood.cn/anna-pao-sohmen-centre-at-shanghai-yk-pao-school-by-scenic-architecture-office.htm
CASE 02 — FTVS, CHARLES UNIVERSITY
FTVS UK — Contacts / faculty pages; sports facilities; CU SPORT Gym.
https://www.ftvs.cuni.cz/en/faculty/contacts
iscus.cz — Haly sportovního centra UK Veleslavín (#19361).
https://iscus.cz/kraje/praha/pasport/19361
iscus.cz — Stadion a venkovní hřiště sportovního centra UK Veleslavín (#19360).
https://iscus.cz/kraje/praha/pasport/19360
Wikipedia (cs) — Vysoká škola politická ÚV KSČ; Fakulta tělesné výchovy a sportu UK.
https://cs.wikipedia.org/wiki/Fakulta_t%C4%9Blesn%C3%A9_v%C3%BDchovy_a_sportu_Univerzity_Karlovy
SlavneVily.cz — Škola ve Veleslavíně (Stavby Prahy 6).
https://www.slavnevily.cz/stavby-/-unesco/stavby-prahy-6/skola-ve-veleslavine
Charles University tenders — UK FTVS block renovation.
https://zakazky.cuni.cz/contract_display_7294.html
STANDARDS USED FOR CHECKS
FIBA Official Basketball Rules 2024.
https://assets.fiba.basketball/image/upload/documents-corporate-fiba-official-rules-2024-v10a.pdf
FIVB Official Volleyball Rules 2025–2028.
https://www.fivb.com/wp-content/uploads/2025/01/FIVB-Volleyball_Rules2025_2028-EN-v05.pdf